## Slide 1
Use a Map and Compass for a Route
Unit MH12CY010 · Agored Cymru Level 2 · Learning in the Outdoors · 3 Credits
LO1
Maps & Compasses
LO2
Create a Route Card
LO3
Complete the Route

## Slide 2
Unit Overview
LO1
Understand the key features of maps and compasses
AC 1.1, 1.2
LO2
Be able to create a route card
AC 2.1
LO3
Be able to complete the planned route
AC 3.1, 3.2
Assessment: mainly practical demonstration — your assessor will observe you completing a real route.
MH12CY010
Use a Map and Compass for a Route

## Slide 3
LEARNING OUTCOME 1
Understand the key features of maps and compasses
Covers AC 1.1, 1.2

## Slide 4
AC 1.1
Types of Maps
OS Landranger — 1:50,000
Covers a wide area. Good for planning a whole day's route.
OS Explorer — 1:25,000
Shows more detail. The standard scale for walking and cycling.
Digital / GPS mapping apps
Show your live position, but should never fully replace a paper map and compass.
MH12CY010
Use a Map and Compass for a Route

## Slide 5
AC 1.2
Baseplate Compass Features
Clear plastic baseplate
Liquid-filled rotating bezel (housing), marked 0–360°
Magnetic needle — red end points to magnetic north
Orienting lines and orienting arrow (inside the housing)
Direction of travel arrow (on the baseplate)
Romer scale — for reading grid references accurately
Magnifying lens and declination scale (on many models)
Silva 1-2-3
System
1. Set the bearing
2. Rotate the compass to align red needle
3. Follow the direction of travel arrow
MH12CY010
Use a Map and Compass for a Route

## Slide 6
LEARNING OUTCOME 2
Be able to create a route card
Covers AC 2.1

## Slide 7
AC 2.1
What Goes on a Route Card?
Distance
Height changes
Route description
Route direction
Pace of group
Stopping points
Exit routes
Points of interest
For this unit: activity must be at least 4 hours, and must include a compass bearing. Walking, cycling and canoeing all count.
MH12CY010
Use a Map and Compass for a Route

## Slide 8
Estimating Timings — Naismith's Rule
Allow 1 hour per 5km, plus 1 minute per 10m of ascent.
This gives a starting estimate — adjust for group fitness, terrain, weather and load carried. Compare your estimate to what actually happens in LO3.
MH12CY010
Use a Map and Compass for a Route

## Slide 9
LEARNING OUTCOME 3
Be able to complete the planned route
Covers AC 3.1, 3.2 — assessed by practical demonstration

## Slide 10
AC 3.1-3.2
On the Day
Complete the route
Your assessor will observe you navigating using map and compass skills for the full planned route (min. 4 hours).
Demonstrate your skills
Taking bearings, using grid references, pacing, and identifying features on the ground.
Review afterwards
Compare your actual timings and route to your route card. Differences are normal — the review is what matters.
MH12CY010
Use a Map and Compass for a Route

## Slide 11
Revision — Key Terms
Grid reference
Exact position on a map
Scale
Map distance vs ground distance
Contour line
Joins points of equal height
Bearing
Direction in degrees, 0–360
Bezel
Rotating dial on a compass
Romer scale
Reads grid references
Declination
Grid north vs magnetic north
Route card
Written journey plan
Leg
One section of a route
Pacing
Counting paces to measure distance
Exit route
Shorter route off the hill if needed
Naismith's Rule
1hr/5km + 1min/10m ascent
MH12CY010
Use a Map and Compass for a Route

## Slide 12
Ready to Get Started?
Open your digital workbook to complete your route card and begin your practical assessment.
MH12CY010NavigationDigital.html