## Slide 1
Pearson BTEC Level 1 Introductory in Sport
PS9 — Map Reading
and Navigation Skills
Bryn Llywarch Outdoor Education | Jonathan Jones
Learning Aim A
Plan a Route Using OS Maps
Learning Aim B
Navigate a Planned Route

## Slide 2
Unit Overview
What you will learn and how you will be assessed
Learning Aim A
A.P1 — Outline route plan, basic map features, 4-figure grid refs
A.P2 — Use appropriate map-reading skills
A.M1 — Detailed plan, 6-figure references, Naismith calculations
A.D1 — Accurate, logical plan with justified route choices
Learning Aim B
B.P2 — Navigate with some assistance, completing sections
B.M2 — Navigate effectively and generally on time
B.D2 — Navigate accurately and independently, self-correcting
Pass
Merit
Distinction
PS9 — Map Reading and Navigation Skills

## Slide 3
LEARNING AIM A
Planning a Route
OS Maps · Scale · Grid References · Contours · Naismith's Rule · Route Cards

## Slide 4
What is an Ordnance Survey Map?
Learning Aim A
OS Explorer 1:25,000
The walker's map. Every 4 cm = 1 km in real life.
• Shows field boundaries, individual buildings
• Shows all footpaths, bridleways, rights of way
• Best for navigation on foot
• Used for DofE expeditions
OS Landranger 1:50,000
The wider picture. Every 2 cm = 1 km in real life.
• Covers a much larger area
• Less detail per square kilometre
• Good for cycling, planning longer journeys
• Less useful for foot navigation
Every OS map contains: Scale | Symbols & Key | Grid lines (Eastings & Northings) | Contour lines | Spot heights
PS9 — Map Reading and Navigation Skills

## Slide 5
OS Map Symbols
You must be able to identify these without a key
Public Footpath
Green dashed line
Public Bridleway
Long green dashes
National Park Boundary
Orange dot-dash line
A-Road
Red solid line
River / Stream
Blue wavy line
Lake / Reservoir
Filled blue area
Marsh / Wetland
Blue tick marks
Coniferous Woodland
Dark green triangles
Non-coniferous Woodland
Light green circles
Contour Line
Brown line + height
Spot Height
Black dot + number
Trig Point
Blue triangle + dot
Car Park
Blue square, white P
Youth Hostel
Blue box — YH
Campsite
Blue triangle
Church with Tower
Black cross + square
PS9 — Map Reading and Navigation Skills

## Slide 6
Scale and Distance
Learning Aim A — A.P2
Map measurement × Scale denominator = Real distance
e.g. 4 cm on a 1:25,000 map → 4 × 25,000 = 100,000 cm = 1,000 m = 1 km
1:25,000 (OS Explorer)
4 cm on map = 1 km real
2 cm on map = 500 m real
1 cm on map = 250 m real
Best for walking and foot navigation
1:50,000 (OS Landranger)
2 cm on map = 1 km real
1 cm on map = 500 m real
0.5 cm on map = 250 m real
Good for cycling and wider planning
PS9 — Map Reading and Navigation Skills

## Slide 7
Grid References
Learning Aim A — A.P1 (4-figure) | A.M1 (6-figure)
Always read EASTINGS first (along the corridor), then NORTHINGS (up the stairs)
Four-Figure Reference
Identifies a 1 km² grid square
Take the easting (left number)
Then the northing (bottom number)
Example: 34 east, 55 north = 3455
Used for general location — Pass standard
Six-Figure Reference
Locates a 100 m area within the square
Divide the square into 10 × 10 tenths
Estimate tenths east, then tenths north
Example: 342 east, 554 north = 342554
Required for Merit and Distinction
PS9 — Map Reading and Navigation Skills

## Slide 8
Contour Lines and Terrain
Learning Aim A — Reading the shape of the land
Brown lines = equal height
Every contour line connects all points at the same height above sea level.
Contour interval = 10 m
On OS Explorer maps, each contour line is 10 metres apart in height.
Closer together = steeper
The more tightly packed the contours, the steeper the gradient.
V pointing uphill = valley
Contour V-shapes that point towards higher ground indicate a valley or stream.
V pointing downhill = spur
Contour V-shapes that point towards lower ground indicate a ridge or spur.
Ring of contours = summit
A closed ring of contours with no opening indicates a hill top.
PS9 — Map Reading and Navigation Skills

## Slide 9
Naismith's Rule
Learning Aim A — A.M1 / A.D1 | Estimating walking time
Devised in 1892 by Scottish mountaineer William Naismith — still used today
Step 1 — Flat Distance
1 hour for every 5 km walked on flat ground
Formula: Distance ÷ 5 = Hours
Example: 7.5 km ÷ 5 = 1.5 hrs = 90 min
Step 2 — Ascent
1 hour for every 600 m of height gain
10 min per 100 m gained
1 min per 10 m gained
Example: 300 m ÷ 600 = 0.5 hrs = 30 min
Step 3 — Add together: Flat time + Ascent time = Total estimated journey time
PS9 — Map Reading and Navigation Skills

## Slide 10
Naismith's Rule — Worked Example
Apply the formula step by step
Scenario: A route is 7.5 km long with 200 m of total ascent
Step 1 — Flat time
7.5 km ÷ 5 = 1.5 hours
= 90 minutes
Step 2 — Ascent time
200 m ÷ 600 = 0.33 hours
= 20 minutes
Step 3 — Total
90 min + 20 min
= 1 hour 50 minutes
⚠ Limitations of Naismith's Rule
Assumes fit walker, easy terrain, no weather issues. Adjust for: heavy pack · fatigue · rest stops · poor visibility · strong wind · mixed-ability group · boggy ground. Always treat as minimum estimate.
PS9 — Map Reading and Navigation Skills

## Slide 11
Producing a Route Card
Learning Aim A — Required for all assessment grades
What goes in a route card?
Leg number
Start grid reference (6-figure for M/D)
End grid reference (6-figure for M/D)
Distance for each leg (km)
Height gain for each leg (m)
Naismith estimated time (minutes)
Terrain notes and hazards
Emergency contact details
Escape route for each leg
Weather forecast
Pass
4+ legs
4-figure grid refs
Basic distance & time
Merit
4+ legs
6-figure grid refs
Full Naismith timings
Distinction
4+ legs, 6-figure refs
Full Naismith working
Route justification + escape routes
PS9 — Map Reading and Navigation Skills

## Slide 12
Risk Assessment
Learning Aim A — Identifying and managing hazards
Risk Level = Likelihood (1–5) × Severity (1–5) | Low: 1–6 · Medium: 7–12 · High: 13–25
Hazard
Likelihood
Severity
Risk Level
Control Measures
Slippery path
3
4
12
Appropriate footwear, slow pace, stick/pole
Sudden weather
2
4
8
Check forecast, carry waterproofs, escape route
Injury / blister
3
3
9
First aid kit, correct kit, break-in boots
Getting lost
2
3
6
Brief group, carry map, buddy system
PS9 — Map Reading and Navigation Skills

## Slide 13
Equipment and the Countryside Code
Learning Aim A — Being prepared and responsible
Essential Kit — Day Walk
OS Map (1:25,000 Explorer)
Compass
Waterproof jacket and trousers
Walking boots with ankle support
Water (minimum 2 litres)
Food and snacks
First aid kit
Fully charged mobile phone
Whistle and torch
Route card and pencil
The Countryside Code
Leave no trace — take all litter home
Close all gates behind you
Keep dogs under control and on leads near livestock
Stay on marked footpaths where required
Respect wildlife, farmland and other walkers
Know your rights — Right to Roam
PS9 — Map Reading and Navigation Skills

## Slide 14
LEARNING AIM B
Navigating a Route
Orienting a map · Tracking progress · Attack points · Handrail features · STOP

## Slide 15
Navigation Techniques
Learning Aim B — B.P2 · B.M2 · B.D2
1. Orient the Map
Turn the map until features on it align with features on the ground. Use a compass to set north. Always navigate with an oriented map.
2. Track Your Progress
Tick off landmarks as you pass them. Use Naismith timing to estimate how far you have walked. Confirm position with a grid reference.
3. Attack Points
Navigate to a clearly identifiable feature close to your target, then take a precise bearing to reach the exact spot.
4. Handrail Features
Follow a linear feature — wall, stream, track, fence — as a natural guide. Reduces reliance on constant compass use.
5. Pacing
Count double-steps to measure distance. Approximately 65 double-paces = 100 m for most adults on flat ground.
6. Tick Features
Identify features along your route that you expect to pass. Tick them off as you go to confirm you are on course.
PS9 — Map Reading and Navigation Skills

## Slide 16
The STOP Method
What to do if you think your group is lost
S
Stop
Do not continue walking. If you keep moving you may get further from where you need to be. Keep the group together and calm.
T
Think
When did you last know exactly where you were? How long have you been walking since then? Which direction were you heading?
O
Observe
Look around for features — hills, valleys, streams, buildings, roads — that you can match to your map. What can you see?
P
Plan
Use what you have observed to identify your position on the map. Agree a plan before moving. Consider whether to continue or use an escape route.
PS9 — Map Reading and Navigation Skills

## Slide 17
Assessment Task A — Plan a Route
Learning Aim A | Open your digital workbook and go to Task A
Using your Digimap OS map extract, plan a route of at least 5 km with a minimum of 4 legs
Your route card must include:
Leg number
Start grid reference — six-figure for M/D
End grid reference — six-figure for M/D
Distance for each leg (km)
Height gain for each leg (m)
Naismith estimated time (minutes)
Terrain and navigation notes
Pass
Merit
Distinction
4-figure refs, basic plan
6-figure refs, Naismith timings
Justified choices + escape routes
PS9 — Map Reading and Navigation Skills

## Slide 18
Assessment Task B — Navigate a Route
Learning Aim B | On the day — log your navigation as you go
Navigate your planned route using your OS map and route card. Record times, landmarks and any deviations.
During the walk — log each leg:
Time started and time finished each leg
Landmarks and tick features passed
Any deviations and how you corrected them
Evidence to collect:
Photographs at checkpoints / navigation features
Audio notes recording your decisions out loud
GPX file from your phone or GPS watch
Pass — B.P2
Navigate with some assistance. Complete most of the route correctly.
Merit — B.M2
Navigate effectively and generally on time. Clear evidence.
Distinction — B.D2
Independent, accurate navigation. Self-correct deviations. Strong evidence.
PS9 — Map Reading and Navigation Skills

## Slide 19
Next Steps
1
Open your digital workbook — PS9NavigationDigital.html
2
Complete the knowledge sections (Maps, Scale, Grid Refs, Contours, Naismith)
3
Plan your route in Task A — upload your Digimap OS map extract
4
Navigate your route and complete the navigation log in Task B
5
Upload photo, audio and GPX evidence in the Evidence section
6
Complete the Checklist and Declaration before handing in